## Slide 1: National High Frequency Radar Network: Applications to Search and Rescue, Spill Response, Vessel Tracking, ….
Scott Glenn
Rutgers University MARACOOS

## Slide 2: Over-the-Horizon HF Radar
Transmits High Frequency (HF) radio waves that follow the salty ocean surface Over the Horizon.
Receives and interprets the backscattered signals.
Operates at 4 frequencies with different ranges and resolutions.
Maps currents, monitors waves, detects tsunamis & detects ships.
Transmitter
Receiver
Mac Mini
Low Power,
Small Footprint

## Slide 3
U.S. National HF Radar Network – 3 Components
Data Flow since 2007
1) 150 HF Radars owned mostly by Universities
2) Operated by
the U.S. IOOS
Regional Associations
3) Linked by
the U.S. IOOS
national data backbone

## Slide 4: HF Radar Maps Surface Currents
National Surface Current Mapping Plan – Multi-use
Superstorm Sandy:
1 Day Before Landfall

## Slide 5: USCG Search And Rescue Statistics
US Coast Guard saves lives:
~3,500/year
(~10/day)
50 years
Despite this heroic effort,
lives are still lost:
~400/year before notification
~200/year after notification
35 years

## Slide 6: USCG Drifter Deployments
Most SAR cases occur in the envisioned HF Radar Network footprint
Self Locating Data Marker Buoys (SLDMB)
for Search And Rescue (SAR)
National HF Radar Network
Notes: Here are the initial deployment positions for our SLDMBs. From these records we selected only those that exceeded 4 days in length

## Slide 7: Surface Currents guide Search And Rescue
Surface Currents
Search And Rescue Optimal Planning System (SAROPS)
Data Acquisition
Data Product Generation & Management

## Slide 8: USCG Current Validation
232 km
154 km
123 km
100 km
Results of a 1-year blind validation study -
For every real drifter deployed at sea:
5000 Virtual Drifters Deployed in SAROPS
Search Areas compared to real drifters every 12 hours
HYCOM 96 hour Search Area
36,000 km2
HF Radar 96 hour Search Area
12,000 km2
Search area reduced by factor of 3
Notes: Here are the initial deployment positions for our SLDMBs. From these records we selected only those that exceeded 4 days in length

## Slide 9
Forecast vs. Observed Surface Current Maps
HyCOM Forecast
06:00
HF Radar Observed
06:00
Forecast & Observations Agree at 06:00 GMT

## Slide 10
Forecast vs. Observed Surface Current Maps
HyCOM Forecast
09:00
HF Radar Observed
09:00
Forecast & Observations Disagree at 09:00 GMT

## Slide 11: U.S. IOOS Responds to Deepwater Horizon
USM HFR
USF HFR
June 2
HFR data informed NOAA
trajectory forecasts
Briefing Blog
127 Briefs
Distributed
HFR validation of SABGOM Forecast combined with satellite detected slicks
Many datasets combined for situational awareness
DHS Impact Award for Rapid Response

## Slide 12: HF Radar Detects Ships Over-the-Horizon
Verification with Emitting Vessels
In Approaches to Chesapeake Bay

## Slide 13
Time of Photos
1
2
3
Photo taken from the Westward Wind
8/27/14 04:55 PM (GMT)
Raw Radar Data: 8/27/14 05:00 - 11:00 PM GMT
AIS Data at 06:53 PM GMT
No Vessels in Vicinity of Westward Wind
Westward Wind
HF Radar Detects Ships Over-the-Horizon
Tracking a Non-Emitting Vessel
with HF Radar off Point Lay, AK
Russian Pribaltika
2
3
1
108 km
Sam M Taalak

## Slide 14
HF Radar Extends AIS & Satellite Coverage
HFR Average Max Range
77 km
AIS Average
Max Range 44 km
Station | Detection Time (Minutes) | Samples
HEMP (5 MHz) | 139 | 9
PORT (25 MHz) | 33 | 11
SILD (25 MHz) | 58 | 11
Satellite Overpass at 16:49 GMT
AIS Test
8 August 2013

## Slide 15: Summary
National HF Radar Network:
Uniquely Maps Coastal Surface Currents a) Hurricane Impacts, b) Search And Rescue b) Spill Response ……
Detects Ships
Monitors Nearshore Waves
Detects Tsunamis
HF Radar on Mona Island, PR

## Slide 16: What U.S. IOOS Needs
National HF Radar Network is incomplete.
HF Radars contributed by academics are aging.
New procurements are required to fill gaps, replace aging systems, and provide spares.
Support for Operations and Maintenance is required by Regional Associations.
Additional backbone components required to transport data and support more national plans.
HF Radar at Point Barrow, AK

## Slide 17: Backups

## Slide 18: National HF Radar Network
Coverage for 20 Feb 2015
150 HF Radars Registered
121 HF Radars Reporting

## Slide 19
Hourly maps of the surface current velocity can be viewed for the previous 24 hours (observed currents) and next 24 hours (predicted tidal currents)
Each point is clickable and will bring up time series plots of observed and predicted speed and direction (pictured)
Text output of time series will also be available
Searchable to find nearest grid point to entered latitude and longitude values
NOAA NOS CO-OPS
PORTS System
High Frequency RADAR
Surface Currents
http://tidesandcurrents.noaa.gov/hfradar/

## Slide 20: Wind Resource Analysis
Now, we can begin to spatially evaluate RUWRF model performance offshore!
RUWRF is the Rutgers University version of the Weather Research and Forecasting model, a real-time 3km atmospheric model run by the RU Coastal Ocean Observation Lab (RUCOOL) for offshore wind energy

## Slide 21: HF Radar Monitors Nearshore Waves
National Waves Plan
Nearshore HF Radar product
Validation with a NOAA Buoy
Codar at Breezy Pt.
Significant Wave Height (m)
NOAA Buoy 44025
13 New Buoys in
Mid Atlantic

## Slide 22: HF Radar Detects Tsunamis
6 km offshore
10 km offshore
14 km offshore
18 km offshore
22 km offshore
Long Beach Island, NJ